# Firmware Update for Alex from the memory card micro SD

- Memory card.

- Rewrite the firmware files on the memory card:

boot_nontrust.bin

total.img

(We can immediately write directly to memory card using a card reader or connect to a PC via a cable USB, select the removable disk)

- Install a memory card micro SD in  Highscreen Alex.

- At el. book Highscreen Alex off (long press of the button "POWER"

- Press and hold the "right" and "Left", then click on the button "Power

- Displayed on the LCD menu engineering BootLoader
(Office through the menu buttons "left" and "return" to confirm the selection-button synchronization.)

7.  BOOTLOADER Update( SDMMC update (Update BOOT, to do this, select the third

menu item "Image Update 
8. After the update restart the device (you can not do, and re-enter the engineering menu BootLoader combination described above). 
9. Choose the 1 st item «Total Update» and wait until the end of the firmware update, then press any key to reboot.
10. Next, you need to make a Hard Reset. To do this, choose one of two ways:

1-st method
Press and hold the "right" and "return". Wait for the menu utilities Android System Recovery.
- Select «Factory Reset»
(Choice by the buttons "right" and "food" to confirm - button "Return").
 Wait for the inscription «Data wipe complete.»
- Select «Reboot now»

2-nd way
Include e-mail. Book Highscreen Alex and wait for the download.
- Click "Settings"

- Select "Memory card and e-RAM. Book

- Click "Return to factory settings."
 

- Press "Reboot device"
 

11. EBook Highscreen Alex is ready to work.